## Slide 1: Example of Chain Flow Scripts Used in My Farm Irrigation System

## Slide 2: A simple example
The first example is from the file utilities_py3.py. This is a python 3 file a does simple functions.

## Slide 3: Example of a definition and execution Part 1
from py_cf_py3.chain_flow import CF_Base_Interpreter
cf = CF_Base_Interpreter() # instanciate chain flow engine
cf.define_chain("delete_cimis_email_data",True)
cf.insert_link( "link_1","WaitTod",["*",9,"*","*" ]) # wait till 9:00 am
#delete emails
cf.insert_link( "link_2","One_Step",[delete_cimis_email.delete_email_files])
cf.insert_link( "link_3","WaitTod",["*",10,"*","*" ]) # wait till 10 am
cf.insert_link( "link_4","Reset",[]) # reset the chain
………………
……………………………………….

## Slide 4: Example of a definition and execution Part 2
cf.define_chain("ntpd",True) # this chain keeps the remote processor time in synch
cf.insert_link( "link_1","Log",["ntpd"] ) # Log is for debugging purposes
cf.insert_link( "link_2", "One_Step", [ntpd.get_time] )
cf.insert_link( "link_3", "Log",["got time"] )
cf.insert_link( "link_4", "WaitEvent",[ "HOUR_TICK" ] ) # Wait For New Hour Event
cf.insert_link( "link_5", "Reset",[] ) # Rest the chain to update time again
cf.define_chain("linux_test",False) # this is a chain to debug this module
cf.insert_link( "linkxx","Log",["test chain start"])
cf.insert_link( "link_0", "SendEvent", ["MINUTE_TICK",1] )
cf.insert_link( "link_1", "WaitEvent", ["TIME_TICK"] )
cf.insert_link( "link_2", "SendEvent", [ "HOUR_TICK",1 ] )
cf.insert_link( "link_3", "WaitEventCount", ["TIME_TICK",2,0])
cf.insert_link( "link_4", "SendEvent", [ "DAY_TICK", 1] )
cf.execute() #execute chain flow chains and do not return

## Slide 5: Example of Cleaning Well Filter
The figure to the right shows the well filter and two valves, the master valve and the cleaning valve.
The well cleaning process is a four step process
Water to irrigation
System
Master
Valve
Cleaning Valve

## Slide 6: Well Cleaning Step 1 – Charge the Line
The purpose of this step is to bring the irrigation lines up to pressure so that pressure in the irrigation lines can back flush the well filter
Well
Filter
Water to irrigation
System
Master
Valve
Cleaning Valve

## Slide 7: Well Cleaning Step 2 – Back Flush
Purpose of this step is to create a backflush from field irrigation system to flush the sand from mesh of the filter
Well
Filter
Water to irrigation
System
Master
Valve
Cleaning Valve

## Slide 8: Well Cleaning Step 3 – Flush inside of filter
In this step both the Master Valve and the Cleaning Valve are opened. The purpose of this operation is to flush sand from inside of the filter
Well filter
Water to irrigation
System
Master
Valve
Cleaning Valve

## Slide 9: Well Cleaning Filter Step 4 -- Shut off
This step returns system to off state.
Master Valve and Cleaning Valve are shut off. System is in Default State
Master
Valve

## Slide 10: Chain Flow Code for Steps 1 and 2
cf.define_chain("clean_filter_action_chain", False) #tested
cf.insert_link( "link_1", "Log", ["Clean Step 1"] )
cf.insert_link( "link_3", "One_Step", [ io_control.disable_all_sprinklers ] )
cf.insert_link( "link_4", "One_Step", [ io_control.turn_off_cleaning_valves ] )# turn off cleaning valve
cf.insert_link( "link_5", "One_Step", [ io_control.turn_on_master_valves ] )# turn turn on master valve
cf.insert_link( "link_6", "WaitTime", [120,0,0,0] )
cf.insert_link( "link_1", "Log", ["Clean Step 2"] )
cf.insert_link( "link_7", "One_Step", [ io_control.turn_on_cleaning_valves ] )# turn on cleaning valve
cf.insert_link( "link_8", "One_Step", [ io_control.turn_off_master_valves ] )# turn turn off master valve
cf.insert_link( "link_9", "WaitTime", [30,0,0,0] )

## Slide 11: Chain Flow Code For Section 3 and 4
cf.insert_link( "link_1", "Log", ["Clean Step 3"] )
cf.insert_link( "link_10", "One_Step", [ io_control.turn_on_master_valves ] )# turn turn on master valve
cf.insert_link( "link_11", "WaitTime", [10,0,0,0] )
cf.insert_link( "link_1", "Log", ["Clean Step 4"] )
cf.insert_link( "link_12", "One_Step", [ io_control.turn_off_cleaning_valves ] )# turn turn off master valve
cf.insert_link( "link_13", "One_Step", [ io_control.turn_off_master_valves ] )# turn turn off cleaning valve
cf.insert_link( "link_14", "One_Step", [ io_control.disable_all_sprinklers ] )
cf.insert_link( "link_15", "One_Step", [ self.clear_cleaning_sum ] )
cf.insert_link( "link_17", "One_Step", [ self.log_clean_filter ] )
cf.insert_link( "link_17", "Terminate", [] )

## Slide 12: Complex Example – Irrigation Control
The irrigation operation consists of three redis data structures. These data structures has to be persistent because of reboots caused by power loss.
The first queue for external processes to place command requests. This includes items like irrigation schedules and web actions.
The second queue is to store the pending irrigation actions. Irrigation actions are queued as a typical irrigation schedule includes many steps.
The third cell is the data structure holding the current irrigation action that is occurring.
There are chains associated with each of these data structures
External Queue
Pending Irrigation Steps
Current Irrigation Step

## Slide 13: Control of External Request Queue
This chain
  Waits for 1 second
  Check external queue for element in redis queue and either process the action or place the elements in the irrigation queue.
  Reset the chain
cf.define_chain( "plc_monitor_control_queue", True )
cf.insert_link( "link_1", "WaitTime", [ 1,0,0,0] ) # wait 1 secod
cf.insert_link( "link_2", "One_Step", [ sprinkler_control.dispatch_sprinkler_mode ] )
cf.insert_link( "link_3", "Reset", [] )

## Slide 14: Process the Second
This chain does the following actions
  Wait 5 second
  Test Second queue
    if empty return Reset
    If not analyize commands
      If non irrigation commands return Reset
      If irrigation command return disable
  sprinkler_element.start() setup the irrigation step and start the irrigation action
  Wait 1 second
  Measure current
  Check current
    If over current flag condition return Reset
    Else return Disable
  Enable 2 working chains discussed next
  Wait for Event Cell Done
  Reset chain irrigation ended
cf.define_chain("monitor_irrigation_job_queue", True ) # tested
cf.insert_link( "link_1", "WaitTime", [ 5,0,0,0] ) # wait 5 seconds
cf.insert_link( "link_2", "Code", [ sprinkler_queue.load_irrigation_cell ] )
cf.insert_link( "link_3", "Code", [ sprinkler_element.start] )
cf.insert_link( "link_4", "WaitTime", [ 1,0,0,0] ) # wait 1 seconds
cf.insert_link( "link_5", "One_Step", [ monitor.measure_current ] )
cf.insert_link( "link_6", "Code", [ sprinkler_element.check_current ] )
cf.insert_link( "link_7", "Enable_Chain", [["monitor_irrigation_cell","monitor_current_sub" ]])
cf.insert_link( "link_8", "WaitEvent", ["CELL_DONE" ] )
cf.insert_link( "link_9", "Reset", [] )

## Slide 15: Current Monitor Thread
This chain is broken out as a separate chain because a irrigation valve can short occur on a solenoid. When that occurs a 4 amp current surge can occur. The sprinkler wire can safely care only 2 amp. Waiting one minute can result in wire damage. A 15 second polling is used in this loop.
The chain is fairly straight forward except for sprinkler_element.check_current, which was described in previous slide.
cf.define_chain("monitor_current_sub", False )
cf.insert_link( "link_0", "Log" , [["monitor_current_sub chain is working"]])
cf.insert_link(
"link_1", "WaitTime", [ 15,0,0,0] ) # wait 15 second
cf.insert_link( "link_2", "One_Step", [ monitor.measure_current_a ] )
cf.insert_link( "link_3", "One_Step", [ sprinkler_element.check_current ] )
cf.insert_link( "link_4", "Reset", [] )

## Slide 16
Processing Steps
  Wait for MINUTE_TICK
  Check Current
  Check For excessive flow Rate
    If flow is excessive then terminate irrigation
  Sprinkler_element.monitor checks for irrigation flags and elapsed sprinkler time.
    If timeout or error condition issue DISABLE return code
    Else issue RESET return code
  Send Event CELL_DONE
  DISABLE This chain and monitor_current_chain
  This example shows hybrid processing chain
cf.define_chain("monitor_irrigation_cell", False ) #Tested
cf.insert_link( "link_1", "WaitEvent", [ "MINUTE_TICK" ] )
cf.insert_link( "link_2", "One_Step", [ sprinkler_element.check_current ] )
cf.insert_link( "link_3", "One_Step", [ sprinkler_element.check_for_excessive_flow_rate ] )
cf.insert_link( "link_3", "Code", [ sprinkler_element.monitor ] )
cf.insert_link( "link_4", "SendEvent", ["CELL_DONE"] )
cf.insert_link( "link_5", "Disable_Chain", [["monitor_irrigation_cell","monitor_current_sub" ]])